## Slide 1
Car Damage Detection
Kaggle Competition | YOLOv8 Object Detection
Apr 30 – May 8
2026
🔍 Task
차량 외관 손상 탐지
(Object Detection)
Dataset
학습데이터 52장 / 검증 데이터 1,043장
테스트용 데이터 698장
Metric
mAP@50
(IoU ≥ 50% 기준)
Detection Classes (14)
• bonnet-dent
• doorouter-dent
• front-bumper-dent
• rear-bumper-dent
• fender-dent
• roof-dent
• quaterpanel-dent
• boot-dent
• Headlight-damage
• Taillight-Damage
• Sidemirror-Damage
• Front-windscreen-damage
• Rear-windscreen-Damage
• Runningboard-Damage

## Slide 2
YOLOv8 최적화 방법 & 성능 결과
Transfer Learning
COCO pretrained YOLOv8s 가중치
- 이미 학습된 데이터셋에 맞게 추가 학습
자동 최적화
AdamW 자동 선택 (lr=0.000556)
Warm-up 3 epoch 적용
데이터 증강
Albumentations: 블러, 명암조정, 흑백, 좌우 반전 등으로 데이터 증강
AMP (자동 혼합 예측)
FP16 연산 → 학습 속도 향상
GPU 메모리 효율 최적화
Chart: 클래스별 mAP50
| Sidemirror | Taillight | Rear-WS | bonnet | doorouter | front-bmpr | Headlight | fender | quaterpnl | rear-bmpr | Front-WS | roof | boot | Running
mAP50 | 0.212 | 0.251 | 0.279 | 0.275 | 0.248 | 0.195 | 0.109 | 0.14 | 0.068 | 0.145 | 0.182 | 0.016 | 0.004 | 0.007
mAP@50
0.152
1 Epoch만 학습 → epoch 증가 시 개선 가능
학습 데이터 52장으로 매우 부족
Pretrained 덕분에 1 epoch에도 동작